## Slide 1: AREN 304 SOIL MECHANICS
INSTRUCTOR: DR. -ING PEACE K. AMOATEY

## Slide 2
Lecture 8 Permeability

## Slide 3: Objectives
  At the end of the lecture, students should understand:
  the Bernouli equation as it applies to flow through soils
  the definition of hydraulic gradient
  understand permeability/hydraulic conductivity
  how to determine hydraulic conductivity in the lab and on the field

## Slide 4: Soil Permeability: A physical property

## Slide 5: Flow of water through soil
  Soils are assemblages of solid particles with interconnected voids where water can flow from a point of high energy to a point of low energy.
  The study of flow water through porous media is important for stability analyses of earth retaining structures (retaining walls, earth dams) subjected to seepage force
There are 2 main issues
  Quantity of water flowing that will be lost by percolation through a dam or its subsoil
  Pore water pressures When water flows pore water pressures change.

## Slide 6: What is Permeability?
The property of soils that allows flow of fluid through its interconnected void space at some rate.
It is a measure of how easily a fluid (e.g. water) can pass through the soil or the measure of the soil’s ability to permit water to flow through its pores or voids
This property is a product of the granular nature of the soil, although it can be affected by other factors (such as water bonding in clays).
Different soils have different permeabilities.

## Slide 7: Importance of Permeability
The permeability of soils has a decisive effect on the :
Estimating the quantity of underground seepage under various hydraulic conditions,
for investigating problems involving the pumping of water for underground construction,
For making stability analyses of earth dams and earth-retaining structures that are subject to seepage forces.

## Slide 8: Importance of Permeability
Estimating the quantity of underground seepage
Solving problems involving pumping seepage water from construction excavation

## Slide 9: Importance of Permeability
Design of filters

## Slide 10
Flow through a Dam
Unsaturated
Soil
Flow of water
Estimating the quantity of water through a dam

## Slide 11: Bernoulli’s Equation
datum
z
fluid particle
Bernoulli's Principle states that as the speed of a moving fluid increases, the pressure within the fluid decreases.
The energy of fluid comprise of:
Potential energy: due to elevation (z) with respect to a datum
Pressure energy: due to pressure
Kinetic energy: due to velocity

## Slide 12: Bernoulli’s Equation
The total head at any point in water under steady flow condition may be expressed as :
Total head = pressure head + velocity head + elevation head

## Slide 13
As the water flows from A to B, there is an energy loss which is represented by the difference in the total heads HA, and HD
where, PA and PB = pressure heads, VA and VB = velocity, g - acceleration due to gravity, γw = unit weight of water, h = loss of head.
For all practical purposes the velocity head is a small quantity and may be neglected.
The loss of head of h units is effected as the water flows from A to B. The loss of head per unit length of flow may be expressed as:
i = h/L
where i is called the hydraulic gradient.
Definition of Hydraulic Gradients

## Slide 14: Definition of Hydraulic Gradient
In the field, the gradient of the head is the head difference over the distance separating the 2 wells.
In the field, the gradient of the head is the head difference over the distance separating the 2 wells

## Slide 15
W.T.
Definition of Hydraulic Gradient
Datum
hA = total head
W.T.
h = hA - hB
Impervious Soil
Impervious Soil
pervious Soil
hB= total head
A
B
L

## Slide 16
W.T.
A
B
Soil
Water In
h =hA - hB
Head Loss or
Head Difference or Energy Loss
hA
hB
i = Hydraulic Gradient
(q)
Water
out
L = Drainage Path
Datum
hA
W.T.
hB
)h = hA - hB
Impervious Soil
Impervious Soil
ZA
Datum
ZB
Elevation Head
Pressure Head
Pressure Head
Elevation Head
Total Head
Total Head
Definition of Hydraulic Gradient

## Slide 17: DARCY'S LAW
Darcy in 1856 derived an empirical formula for the behavior of flow through saturated soils.
He found that the quantity of water q per sec flowing through a cross-sectional area of soil under hydraulic gradient i can be expressed by the formula.
or the velocity of flow can be written as
where k is termed the hydraulic conductivity (or coefficient of permeability) with units of velocity. v is discharge velocity which is the quantity of water flowing in unit time through a unit gross cross-sectional area of soil at right angles to the direction of flow.
  A is the cross-sectional area of soil normal to the direction of flow
Darcy’s law is suitable for fine grained types of soils.

## Slide 18
Flow (volume per unit time) was
    proportional to the head difference Dh
    proportional to the cross-sectional area A
    inversely proportional to the length of sample DL
Darcy’s Law: Water flow through soil
Soil Sample

## Slide 19
Thus
Then the quantity of water flowing through the soil per unit time is
Equation (2a) may be written as
where i = the hydraulic gradient
v = Q/A the Darcy or superficial velocity
k = v/i is the hydraulic conductivity (or coefficient of permeability)
Darcy’s Law: Water flow through soil
(2a)

## Slide 20: Determination of hydraulic conductivity of soils
The hydraulic conductivity k is a measure of how easy the water can flow through the soil.
The hydraulic conductivity is expressed in the units of velocity (such as cm/sec and m/sec).
Methods that are in common use for determining the coefficient of permeability k can be classified as:
  Laboratory methods: Constant head permeability method and falling head permeability method
  Field methods: Pumping tests, Bore hole tests
  Indirect Method: Empirical correlations

## Slide 21
Manometers
L
inlet
outlet
H
constant head
device
device for flow
measurement
load
porous disk
Fig. 4 Constant Head Permeameter
sample
Laboratory Measurement of Permeability

## Slide 22
Constant Head Test
Notes: For coarse-grained soils

## Slide 23: Constant Head Permeability Test
The sample of length L and cross-sectional area A is subjected to a head h which is constant during the progress of a test.
A test is performed by allowing water to flow through the sample and measuring the quantity of discharge Q in time t.
The constant head permeameter test is more suited for coarse grained soils such as gravelly sand and coarse and medium sand.
or k=

## Slide 24
The volume discharge X during a suitable time interval T is collected.
The difference in head H over a length L is measured by means of manometers.
Knowing the cross-sectional area A, Darcy’s law gives
It can be seen that in a constant head permeameter:
Constant Head Permeameter
k (3)

## Slide 25
H2
H1
H
L
Fig. 5 Falling Head Permeameter
Standpipe of
cross-sectional
area a
Sample
of area A
porous disk
Laboratory Measurement of Permeability
The falling head test is
mainly for fine-grained
soils.

## Slide 26
Analysis
H2
H1
H
L
Standpipe
of area
a
Sample
of area
A
Consider a time interval dt
The flow in the standpipe =
The flow in the sample =
and thus
(4a)
Falling Head Permeameter

## Slide 27
H2
H1
H
L
Standpipe
of area
a
Sample
of area
A
Solution
-
=
a
dH
dt
kA
H
L
(4
a)
Equation (4a) has the solution:
-
=
+
a
n
H
kA
L
t
cons
t
l
(
)
tan
(4
b)
Initially H=H
1
at time t=t
1
Finally H=H
2
at time t=t
2.
k
aL
A
n
H
H
t
t
=
-
l
(
/
)
1
2
2
1
(4
c)
Falling Head Permeameter

## Slide 29
10-1
10-2
10-3
10-4
10-5
10-6
10-7
10-8
10-9
10-10
10-11
10-12
Gravels
Sands
Silts
Homogeneous Clays
Fissured & Weathered Clays
Typical Permeability Ranges (metres/second)
Typical Permeability Values
Soils exhibit a wide range of permeabilities and while particle size may vary by about 3-4 orders of magnitude permeability may vary by about 10 orders of magnitude.

## Slide 30
Hydraulic conductivity of soils depends on several factors:
    Fluid viscosity (h): as the viscosity increases, the hydraulic conductivity decreases
    Pore size distribution
    Temperature
    Grain size distribution
    Degree of soil saturation
Hydraulic Conductivity
It is conventional to express the value of k at a temperature of 20oC.

## Slide 31: Hydraulic conductivity of some soils

## Slide 32: Hydraulic Conductivity, k

## Slide 33: Field Determination of Hydraulic Conductivity
Steps
Water is pumped out at a constant rate from a test well that has a perforated casing.
several observation wells at various radial distances are made around the test well.
Continuous observations of the water level in the test well and in the observation wells are made after the start of pumping, until a steady state is reached.
The steady state is established when the water level in the test and observation wells becomes constant.

## Slide 34: Transmissivity
It is measured as the rate at which groundwater is transmitted through a unit width of an aquifer under a unit hydraulic gradient.
It is expressed as the product of hydraulic conductivity and the thickness of the aquifer:
Where
    T = transmissivity, or.
    k = hydraulic conductivity, cm/sec.
    b = aquifer thickness, m.

## Slide 35: Transmissivity

## Slide 36: Pumping Well with Observation Holes
In the field, the average hydraulic conductivity of a soil deposit in the direction of flow can be determined by performing pumping tests from wells.
The top permeable layer, whose hydraulic conductivity has to be determined, is unconfined and underlain by an impermeable layer.
During the test, water is pumped out at a constant rate from a test well that has a perforated casing.
Several observation wells at various radial distances are made around the test well.

## Slide 37: Pumping Well with Observation Holes
Continuous observations of the water level in the test well and in the observation wells are made after the start of pumping, until a steady state is reached.
The steady state is established when the water level in the test and observation wells becomes constant.
The expression for the rate of flow of groundwater into the well, which is equal to the rate of discharge from pumping, can be written as:

## Slide 38: Pumping Well with Observation Holes
Continuous observations of the water level in the test well and in the observation wells are made after the start of pumping, until a steady state is reached.
The steady state is established when the water level in the test and observation wells becomes constant.
The expression for the rate of flow of groundwater into the well, which is equal to the rate of discharge from pumping, can be written as:

## Slide 39: Pumping Well with Observation Holes
Aquifer: Soil or rock forming stratum that is saturated and permeable enough to yield significant quantities of water (e.g. sands, gravels, fractured rock)
Unconfined Aquifer (water table aquifer) is an aquifer in which the water table forms the upper boundary.
Confined Aquifer is an aquifer confined between two impervious layers (e.g. clay).

## Slide 40: Summary
1. The flow of water through soils is governed by Darcy's law, which states that the average flow velocity is proportional to the hydraulic gradient.
2. The proportionality coefficient in Darcy's law is called the coefficient of permeability or hydraulic conductivity, k.
3. The value of k is influenced by the void ratio, particle size distribution, and the wholeness of the soil mass.
4. Homogeneous clays are practically impervious while sands and gravels are pervious.

## Slide 41: EXAMPLES
The constant-head permeability test arrangement shown below. A test gives these values:
L = 30 cm
• A = area of the specimen = 177 cm2
• Constant-head difference, h =50 cm
• Water collected in a period of 5 min =350 cm3
Calculate the hydraulic conductivity in cm/sec.

## Slide 42: EXAMPLES
Given that:
L = 30 cm
• A = area of the specimen = 177 cm2
• Constant-head difference, h =50 cm
• Water collected in a period of 5 min =350 cm3

## Slide 43: Examples

## Slide 44: Exercise

## Slide 45: Examples
For a falling-head permeability test, the following values are given:
• Length of specimen 8 in.
• Area of soil specimen 1.6 in.2
• Area of standpipe 0.06 in.2
• Head difference at time t 0 20 in.
• Head difference at time t 180 sec 12 in.
Determine the hydraulic conductivity of the soil in in./sec.

## Slide 46: Home Work
Examples 7.1 to 7.5  Das, Chapter 7

## Slide 47: Exercise
A constant head permeability test was carried out on a cylindrical sample of sand 5 cm in diameter and 15 cm in height. 40 cm3 of water was collected in 5 secs, under a head of 30 cm. Compute the hydraulic conductivity in cm/s and the velocity of flow in cm/sec if porosity is 0.6.

## Slide 48: Problems
1. A 300mm diameter test well penetrates 27 m below the static water table. After 24 hours of pumping at 69 litres/sec, the water level in an observation well at a distance of 95m form the test well is lowered 0.5 m and the other observation well at a distance of 35m m form the test well at a distance of 35 m from the test well, the drawdown is 1.1 m.
a. What is the rate of flow in cubic meters per day?
b. Compute the coefficient of permeability of the aquifer in meters per day.

## Slide 49: Problems
2. A pumping test was performed in a well a confined aquifer to evaluate the coefficient of permeability of the soil in the aquifer. When equilibrium flow was reached, the following data were obtained:
a. Equilibrium discharge of water from the well is 200 cm³/sec.
b. Water levels ( and ) = 6 and 4.5m and at distances from the well ( and ) of 36 and 18m, respectively.
c. Thickness of aquifer is 5m.
Find the hydraulic conductivity (cm/day).

## Slide 50: Problems
4. A well is constructed to pump water from a confined aquifer. Two observation wells are constructed at distances of 100 m and 1000 m respectively. Water is pump from the pumping well at a rate of 0.2 m³ /min. At steady state, the drawdown is observed as 2m and 8m respectively in the farthest and the nearest observation wells. Diameter of the test well is 1m. The thickness of the aquifer is 20 m.
a. Determine the hydraulic conductivity in cm/sec.
b. Determine the transmissivity in cm²/sec.
c. Determine the drawdown in the test well.

## Slide 51: Problems

## Slide 52: Problems
5. A certain 20 m thick sandy aquifer has a transmissivity of 0.12 m²/sec and a void ratio of 0.91. Ground water is flowing through this aquifer with a hydraulic gradient of 0.0065.
a. Compute the hydraulic conductivity of the sand aquifer.
b. Compute the seepage velocity.
c. How much time would be required for water to travel 1km through this aquifer?

## Slide 53: Problems
6. Refer to the constant-head arrangement shown in Figure 7.5. For a test, the following are given.
L =18 in.
A = area of the specimen = 3.5 in.2
Constant-head difference, h = 28 in.
Water collected in 3 min = 21.58 in.3. Calculate the hydraulic conductivity (in./sec).

## Slide 54: Problems
7. For a falling-head permeability test, the following are given:
• Length of the soil specimen = 20 in.
• Area of the soil specimen = 4 in.2
• Area of the standpipe = 0.2 in.2
• Head difference at time t = 0 is 30 in.
• Head difference at time t = 10 min is 12 in.
Determine the hydraulic conductivity of the soil (in./min).
What was the head difference at time t = 5 min?

## Slide 55: Try Problems
1. At one location on the ground a porous layer lies above an impervious stratum. The thickness of this porous layer is 7 meters. Water table also lies in the porous layer and it is at the depth of 1.5 m below the ground surface. A test well is drilled into the ground which penetrates the whole thickness of this permeable layer. Through this well the water is pumped out at the rate of 100 litres/sec. The drawdown of the water table because of this pumping out is observed by making observation wells at a distance of 7 m and 21 m from the test well. The drawdown observed at 7 m is 3 m and at 21 m it is 0.8 m.
What is the coefficient of permeability of that porous layer of soil?

## Slide 56: Try Problems
2. At one location on the ground a porous layer is observed between two impervious layers of soil. The porous layer, which has the thickness of 4 m, lies under the impervious soil layer of thickness 5 m. A test well is drilled into the ground which penetrates the whole thickness of this permeable layer. Through this well the water is pumped out at the rate of 20 L/sec. The influence of this pumping out on water level is observed by making observation wells at a distance of 5 m and 11 m from the test well. The water level in these well is observed at 3.5 m and 3m below the ground surface in 5 m and 11 m distant well respectively. What is the coefficient of permeability of that porous layer of soil?

## Slide 57: Try Problems
3. For a falling-head permeability test, the following are given:
• Length of soil specimen = 700 mm
• Area of the soil specimen = 20 cm2
• Area of the standpipe = 1.05 cm2
• Head difference at time t = 0 is 800 mm
• Head difference at time t = 8 min is 500 mm
Determine the absolute permeability of the soil.
What is the head difference at time t 6 min? Assume that the test was conducted at 20℃, and at 20℃, 𝛾_𝑤 = 9.789 kN/m3 and 𝜂 = 1.005 x 10-3 N.s/m2 .